## Slide 1
CAN BUS
INTRUSION
ID: 0x666
DIFF > 350
CAN BUS INTRUSION
DETECTION SYSTEM
Physical-Layer Authentication for In-Vehicle Networks
ESP32 • CAN Bus (TWAI Driver) • Analog Signal Fingerprinting • Real-Time Alert System

## Slide 2
THE PROBLEM
✕ No Authentication
CAN Bus was designed in the 1980s for reliability — not security. Any node on the bus can send any message with any ID, with zero verification.
⚠ Spoofing Attacks
Attackers can inject malicious CAN frames using unknown node IDs (e.g. 0x666) to manipulate critical vehicle systems like speed or braking.
? No Intrusion Detection
Standard ECU setups have no mechanism to detect whether a message is from a legitimate ECU or from a rogue attacker node physically plugged into the bus.

## Slide 3
SYSTEM ARCHITECTURE
Green = Legitimate nodes | Red = Attacker node | Blue = Surveillance node | Yellow = CAN Bus lines

## Slide 4
HOW CAN BUS COMMUNICATION WORKS
SENSOR
DETECTS
EVENT
▶
ECU
PROCESSES
DATA
▶
CAN
TRANSCEIVER
SENDS FRAME
▶
ALL NODES
RECEIVE
MESSAGE
CAN FRAME STRUCTURE
SOF
1 bit
IDENTIFIER
11 bits
RTR
1 bit
DLC
4 bits
DATA
0–64 bytes
CRC
15 bits
ACK
2 bits
EOF
7 bits
⚠ The IDENTIFIER field determines message priority and source — but CAN protocol has NO authentication to verify it is genuine.

## Slide 5
DETECTION METHODOLOGY
PHYSICAL LAYER SAMPLING
ADC pin (GPIO 34) samples the CAN bus voltage in real time
50 samples collected over ~1 ms using analogRead() at 12-bit resolution
MAX – MIN voltage difference (DIFF) computed for each received message
Legitimate ECUs produce consistent, low-noise analog signatures
Rogue nodes produce higher variance due to different hardware characteristics
AUTHENTICATION LOGIC
1
Receive CAN frame
2
Check if ID is known (0x101 or 0x102)
3
Compute DIFF from ADC samples
4
Compare DIFF against trained threshold (350)
5
If DIFF > threshold or unknown ID → increment abnormalCount
6
If abnormalCount ≥ 3 → INTRUSION ALERT

## Slide 6
HARDWARE SETUP & NODE ROLES
SPEED ECU NODE
CAN ID: 0x101
GPIO 5 (TX) / GPIO 4 (RX)
Sends 1-byte payload (speed=60)
Triggered by button press
500 kbps CAN bus speed
Represents legitimate node
BRAKE ECU NODE
CAN ID: 0x102
GPIO 5 (TX) / GPIO 4 (RX)
Sends 1-byte payload (brake=1)
Triggered by button press
500 kbps CAN bus speed
Represents legitimate node
ATTACKER NODE
CAN ID: 0x666
GPIO 5 (TX) / GPIO 4 (RX)
Sends 0xFF payload
Aggressive 20ms interval
Unknown/spoofed CAN ID
Simulates rogue injection
SURVEILLANCE NODE
IDS Monitor
ADC on GPIO 34
LCD I2C on 0x27
Buzzer on GPIO 27
Monitors CAN-H/CAN-L
Displays & alerts in real-time

## Slide 7
THRESHOLD CALIBRATION & RESULTS
350
SPEED THRESHOLD
(ADC DIFF Units)
350
BRAKE THRESHOLD
(ADC DIFF Units)
3×
CONSECUTIVE HITS
BEFORE ALERT
ANALOG SIGNATURE COMPARISON (ADC DIFF)
0
200
350
500
← THRESHOLD
210
Speed ECU
(0x101)
195
Brake ECU
(0x102)
520
Attacker
(0x666)

## Slide 8
ALERT SYSTEM & REAL-TIME OUTPUT
LCD DISPLAY
Normal mode:
"SPEED ECU | STATUS: UPDATED"
Checking:
"CHECKING..."
Alert mode:
"INTRUSION ALERT | UNKNOWN NODE"
16×2 I2C LCD at address 0x27 refreshes on every received frame
SERIAL MONITOR
OK:
"[OK] SPEED ECU | DIFF=210"
OK:
"[OK] BRAKE ECU | DIFF=195"
Alert:
"[ALERT] UNKNOWN NODE | ID=0x666 | DIFF=520"
115200 baud serial output with timestamped CAN ID and DIFF values
BUZZER ALERT
Normal:
Buzzer OFF (GPIO 27 = LOW)
Anomaly 1-2:
Buzzer OFF — still checking
Anomaly ≥ 3:
Buzzer ON — sustained alert
Persistent buzzer activation until legitimate traffic resets abnormal counter

## Slide 9
CONCLUSION & FUTURE SCOPE
✓ ACHIEVED
Physical-layer fingerprinting using ADC differential analysis
Real-time detection of spoofed CAN IDs (0x666 attacker)
Multi-node CAN bus simulation on ESP32 hardware
Zero-false-positive design with 3-hit confirmation window
Dual alert output: LCD + buzzer for immediate visibility
→ FUTURE SCOPE
Machine learning-based anomaly detection on bus traffic patterns
CAN FD support for next-generation automotive ECUs
Cryptographic message authentication (CMAC / AES-based)
OBD-II port deployment for real vehicle integration
Cloud dashboard for fleet-wide intrusion monitoring
By combining CAN ID whitelisting with physical-layer analog fingerprinting, this system detects intrusions that purely software-based solutions would miss — adding a critical hardware-level trust boundary to in-vehicle networks.